## Slide 1
EEGpal: a new graphical user interface for performing automatic and semi-automatic EEG processing and analysis
Michael Mouthon, Michael De Pretto & Selma Aybek
Faculty of Science and Medicine, Section of Medicine, Department of Neuroscience and movement science, University of Fribourg
EEGpal is an open-source Matlab-based software for automated/semi-automated EEG data pre-processing and analyses. It proposes Graphical User Interfaces (GUIs) that allow EEG pre-processing to be batched across participants with a high degree of flexibility in processing parameters. The purpose is to offer a complement to the free software Cartool and an alternative to the original eeglab GUI.
EEGpal
Bridge Detection
s
ICA
ICA decomposition ignoring bad channel
Manual of automatic inspection of components
Use the ICAlabel
toolbox to help components recognition
Topography and trace are displayed simultaneously for each component
Recomposition of the signal without bad components
Batch
Program the sequence of steps to be executed automatically.
Interpolation
Automatic suggestions of bad channels (bridges + Clean Raw Data)
Manual customization of channels selection for interpolation.
Export/Import of interpolation table to work in Excel
Interpolation with 3D_Spline (Cartool) or Spherical (eeglab) algo
Analysis
Epoching/Averaging
Baseline correction
Averaging within or between subject
Save all good epochs into one file or save one file per epoch.
Automatic Epochs rejection based on :
Absolute Amplitude
Step change
Amplitude range
Automatic peak amplitude and latency extraction
Frequency analysis with Power Spectral density (PSD)
Statistic on tracks with T-test or ANOVA
Filtering+
Notch Filter or CleanLine toolbox
Resample data
Filtering with Matlab or eeglab function
Clean Raw Data toolbox with:
ASR
Automatic bad channel suggestion